## Slide 1
  A high-order accurate and monotonic advection scheme is used as a local interpolator to redistribute the concentration onto the adapted grid:
  Three-dimensional adaptation may be fully unconstrained or vertically constrained, maintaining cell area constant throughout each stack of cells:
  Refinement is achieved by repositioning grid nodes in response to three-dimensional adaptation weight field:
  Key features:
  Dynamic adaptation with simultaneous horizontal and vertical grid refinement
  Total number of nodes and connectivity do not change during the simulation
  A local coordinate transformation into a boundary-conforming curvilinear coordinate system is applied to use the air quality model’s original solution algorithms on adapting grid
  Grid adaptation is achieved applying a 4-step iterative process
  Adaptive grid modeling can reduce artificial diffusion in CTMs and improve performance:
Motivation
Adaptive grids can be used to enhance the multiscale capabilities of grid-based air quality models. The technique is used to increase solution accuracy by dynamically refining the modeling grid in response to a model variable or parameter. Nearly all prior adaptive grid air quality modeling has been limited to horizontal refinement and vertical adaptation has not yet been explored in operational models. However, full three-dimensional grid adaptation would be valuable in simulations featuring concentrated plumes in the free troposphere, as well as plumes near inversions or the top of the boundary layer. Here a three-dimensional adaptive grid algorithm designed for chemical transport models is presented. The mesh-moving (r-refinement) method allows vertical and horizontal refinement to occur simultaneously yet retains a grid’s original structure, enhancing compatibility with existing air quality models. Advection tests are used to demonstrate the algorithm’s ability to better capture concentration gradients in atmospheric plumes.
1. Grid cell weighting
Contact Information
M. Talat Odman
School of Civil and Environmental Engineering
Georgia Institute of Technology
odman@gatech.edu
2D Adaptive Grid in CMAQ
Adaptive grid dispersion test 1
Recommendations and challenges
3-D adaptation can benefit simulations of concentrated plumes in the free troposphere or near the top of the PBL where vertical grid resolution is typically coarse
Vertically constrained adaptation may simplify implementation into existing models
Global interpolation algorithms highly recommended for 3˗D adaptation
Overall model resolution is still limited by resolution of meteorology and emissions inputs
Atmospheric plume modeling with a three-dimensional refinement adaptive grid method
M. Talat Odman, Yongtao Hu; School of Civil and Environmental Engineering, Georgia Institute of Technology
Fernando Garcia-Menendez; Center for Global Change Science, Massachusetts Institute of Technology
PM2.5 (µg m-3)
Adaptive Grid
Fixed Grid (4km)
3-D Adaptive Grid Algorithm
2. Grid Movement
Unconstrained adaptation:
Vertically constrained adaptation:
a) µg m-3
c) µg m-3
b) Adaptation Weight
d) Adaptation Weight
3. Field Redistribution & 4. Grid Convergence
z
y
x
Computational Domain
Physical Domain
ζ
η
ξ
  Weights are assigned to each grid cell using a weight function based on model variables or parameters:
Otherwise to Step 1
E
Pollutant puff shown as a three-dimensional iso-surface bounded by PM2.5 concentration equal to 10 µg m-3 crossing an intersection of X and Y grid planes. Grid lines and PM2.5 concentrations (µg m-3) along the planes are also included.
Side view of the adjusted weight fields (b and d) estimated from (a) blank and (c) single-cell-value concentration fields (µg m-3).
Side view of grid response to a normalized weight field using unconstrained adaptation and vertically constrained three-dimensional adaptation
  Iterative grid adaptation continues until one of the grid convergence criteria is met:
  → either the grid nodes do not move significantly
  → or maximum number of iterations is reached
Side view of three-dimensional iso-surfaces defined by PM2.5 concentration equal to 10 μg m-3 in fixed and adaptive grid simulations 1, 5, and 10 hours after release of pollutant puff.
  Advection of an instantaneous pollutant puff under WRF-generated wind field:
Adaptive grid dispersion test 2
Unconstrained
adaptation:
Vertically
constrained
adaptation:
Y grid plane intersecting pollutant puff 5 hours after release simulated with unconstrained adaptation and vertically constrained three-dimensional adaptation. Maximum concentrations predicted by fixed and adaptive grid simulations are shown in adjacent plot.
  Three-dimensional refinement can improve simulations of continuous point sources by retaining higher concentrations along plume centerlines and reducing numerical diffusion:
Adaptive Grid
Fixed Grid
Top view of PM2.5 concentrations (µg m-3) simulated at 2000 m AGL under southeasterly wind field using fixed and adaptive grids
Side view of PM2.5 concentrations (µg m-3) simulated under uniform vertical wind field using fixed and adaptive grids